## Slide 1: Contingency Management in Wetlands
Paul R. Krause, Ph.D.
Knowledge Management Program
Sensitive Ecosystem Workshop Bogota, Colombia November 2012

## Slide 2: Contingencies for Impacts
The largest impacts related to E&P activities in wetlands are spills and erosion
Spills from operations, pipelines, transportation activities all can introduce contaminants into the wetland at different levels
Infrastructure development and operations can enhance erosion throughout the wetland
  Spill Response - Basics
  Erosion Control - Tools

## Slide 3: Oil Spill Response
The world’s leading sustainability consultancy

## Slide 4: Spill Response Basics
Typical Spill and Response Timeline
Initial Response – Stop the Leak
Agencies and Unified Command formed under Incident Command System Shoreline Cleanup and Assessment Teams mobilized
Someone Notices
Second Phase – Containment
SCAT and Containment teams operate through ICS
Third Phase – Cleanup
SCAT and cleanup teams operate for closure of the spill
Incident Occurs
Final Phase – Restoration
ICS is disbanded
Responsible Party takes responsibility for remediation/mitigation

## Slide 5: Spill Response - Command Structure
  Incident Command System (ICS)
  Command Structure of Agencies
    Coordinates the function of response Agencies
      Federal
      State
      Local
      Responsible Party (RP)
  ICS was formed from the response to wildfires
    First implemented in 1989 San Francisco earthquake
      September 11 attack
      Hurricanes Rita, Katrina, Sandy
      Other natural or public disasters
        Deepwater Horizon
  United States Coast Guard is lead Federal Commander
  Unified Command = Federal, State, and RP leads

## Slide 6: Deepwater Horizon ICS

## Slide 7: Spill Response - SCAT
  Shoreline Clean up and Assessment Team (SCAT)
  Function to collect real-time data and provide feedback to the ICS
    Shoreline type – Beach, wetland, rocky shore, coral reef
    Accessibility – Can the oil be accessed by clean up crews?
    Oiling conditions – How much oil, type of oil?
    Logistics – How does the clean up crew access the area? When?
    Need for cleanup – Does this area need clean up?
  Collect chemical data
    Hydrocarbon fingerprint data
      Water
      Sediment
  Identify clean up strategy
  Identify resources at risk
    Habitat
    Population

## Slide 8: Spill Response - Containment
  Oil Containment Technology - Booming

## Slide 9: Spill Response - Collection
  Oil Collection Technology - Skimming

## Slide 10: Spill Response – Other Methods
  Absorbent Pads
  Manual Herding
  Pressure Washing
  Oil Vacuum Suction

## Slide 11: Spill Response - Dispersants
  Oil Collection Technology - Dispersants

## Slide 12: Spill Response – In-Situ Burning
  Burning is most effective way to remove hydrocarbons
  Can be done at sea or on land
  Requires specialized fire-resistant boom at sea
  Multiple hazards associated with burning
    Loss of control
    Air quality issues
    Habitat destruction

## Slide 13: Erosion Control
The world’s leading sustainability consultancy

## Slide 14: Erosion Control - Wetland
  Erosion can be stopped or contained before it creates a problem.
  Sediment transport should be monitored regularly
    Utilize Best Management Practices for erosion control
      Regulate traffic to reduce soil destruction
        Foot Traffic
        Vehicle Traffic

## Slide 15: Erosion Control - Wetland
  Erosion can be stopped or contained before it creates a problem.
  Shoreline protection
    Armoured Mats
  Construction Protection
    Protective waddles
    Silt fences

## Slide 16: Conclusions
  Oil spills and Erosion are major impacts on wetland habitats
  Oil spill protection requires a robust spill response strategy
    Incident Command System
    SCAT Teams
    Data collection
  There are many technologies available to fight spills
  Erosion can be controlled before and during project activities

## Slide 17: Effects on Wetland Function or Service
Any Questions?

## Slide 18
www.erm.com